## Slide 1: Voltiris
Low-Level Software Communication Detailed Specifications V1.2 (2023-07-16)

## Slide 2: Tracklog
Add-ons from version 1.1:
Changing from INI to JSON and from global description “file” to individual options.
Features not implemented are highlighted in yellow
Add-ons from version 1.0:
Create two distinct commands: one for Hard Reset (0x00) and the second for ID Reset (0x01)
Add Broadcast field in the configuration section (ID can be retrieved via the Slave Identification command)
Remove ID in the configuration section
Adding Firmware Update command
Specify how to encrypt configuration section

## Slide 3: Introduction
Accessible Memory Registers
Hard Reset Command
Reset Slave ID Command
Slave Identification
Error message
Options
Firmware update

## Slide 4: Accessible Memory Registers / Commands
Address | Type | Read / Write | Description
0x00 | Command | Write | Hard Reset command
0x01 | Command | Write | Reset Slave ID command
0x02 | Command | Read | Slave Identification command
0x10 | Command | Write | [NOT IMPLEMENTED] Firmware Update command
0x20-0x50 | Command | Read | Get the description of an option (Option0 = 0x20, Option1 = 0x21)
0x51 – 0xFF | Reserved |  | 
0x100-0x101 | uint16 | Read | Version of the memory register (currently 0)
0x102-0x1ff | Reserved |  | 
0x200-0x2fe | uint16 | R/W | Space for memory operations
0x300-0x3ff | uint16 | R/W | Space for options operations
Read / write operations take place in space 0x000-0x3fff. Accessing an invalid address space generates an error respomse.

## Slide 5: Hard Reset command (1/2)
This command can be broadcasted to all slaves on the bus (0x00) or targeted to a specific slave address
Hard reset will reboot the slave Firmware and make it ready for pairing
No Modbus answer expected from this command.
Modbus QUERY | Value | Description
Slave address | 0x00 | Command broadcasted to all slaves
Function | 0x10 | Preset Multiple Registers
Starting Address Hi | 0x00 | Hard Reset cmd.
Starting Address Lo | 0x00 | Hard Reset cmd.
No. of Registers Hi | 0x00 | No data
No. of Registers Lo | 0x00 | No data
Byte count | 0x00 | No data section
Error Check | CRC | 
Example to Hard Reset all slaves on the bus

## Slide 6: Hard Reset command (2/2)
Master
Slave 0x10
Hard Reset broadcasted
Slave will perform a full firmware reset and restart a pairing operation
Note that slaves will take a random ID between 1 and 33
Slave 0x1A

## Slide 7: Reset Slave ID command (1/3)
This command can be broadcasted to all slaves on the bus (0x00) or targeted to a specific slave address
It asks the targeted slave(s) to change their ID and take a new one that is not set in the mask
A 32bits mask is provided in the data section. Bits with 1 means address is already attributed. New slave ID should only be in the available set. For example, 0x0003 means Slave IDs 2 and 3 are already taken, new Slave ID is randomly selected in the range 1-33 (except values 2 and 3)
No Modbus answer expected from this command.
Modbus QUERY | Value | Description
Slave address | 0x10 | Target slave(s) with this ID
Function | 0x10 | Preset Multiple Registers
Starting Address Hi | 0x00 | 
Starting Address Lo | 0x01 | Reset Slave ID cmd.
No. of Registers Hi | 0x00 | 
No. of Registers Lo | 0x02 | Two 16 bits registers are required to store the mask (0x0002)
Byte count | 0x04 | 2 * 16 bits registers = 4 bytes
Data Hi | 0x00 | Slave ID 1 and 2 are already attributed.
2 * Data | 0x00 | 
Data Low | 0x03 | Slave ID 1 and 2 are already attributed.
Error Check | CRC | 
Reset slaves with ID 0x10. New ID is in the range 1-33 bot not 1 nor 2

## Slide 8: Reset Slave ID command (2/3)
Master
Slave 0x10
Reset Slave ID 0x10
Mask is 0b00000000000000000000000010010001
Another Slave ID is randomly selected within range 1-33 except IDs 1, 5 or 8
Note that slaves should take a random ID between 1 and 33
Slave 0x02

## Slide 9: Reset Slave ID command (3/3)
Reset Slave ID 0x05
Mask is 0b00000000000000000000000010010001
Master
Slave 0x05
As slave ID is in the list, slave will do nothing

## Slide 10: Slave identification command (1/4)
Broadcast not supported
Ask a slave to retrieve its 64 bytes unique ID. ID is represented in big endian
Also used to check if multiple slaves have the same ID. In case of collision, CRC will be invalid (and master will further ask slaves with this ID to Reset Slave ID)
Modbus QUERY | Value | Description
Slave address | 0x01 | Target slave with this ID
Function | 0x04 | Read Input Registers
Starting Address Hi | 0x00 | Slave identification cmd.
Starting Address Lo | 0x02 | Slave identification cmd.
No. of Points Hi | 0x00 | 
No. of Points Lo | 0x04 | 4 * 16 bits = 64 bits register
Error Check | CRC | 
Ask slave(s) with ID = 0x01 to retrieve its/their 64 bits unique ID

## Slide 11: Slave Identification command (2/4)
Slave 1 returns its 64 bits unique ID: 0x00 … 04
Modbus ANSWER | Value | Description
Slave address | 0x01 | Target slave with this ID
Function | 0x04 | Read Input Registers
Byte Count | 0x08 | 
Data Hi | 0x00 | Serial number
6 * Data | … | 
Data low | 0x04 | 
Error Check | CRC | 
Slave 1 returns its 64 bits unique ID

## Slide 12: Slave identification command (3/4)
Master
Slave 0x0F identification
Timeout  No slave 0x0F detected, continue searching
Slave 0x10
Slave 0x07
Slave 0x10 identification
Slave 0x10 returns unique ID
Correct CRC. Add slave 0x10 in the valid identified list

## Slide 13: Slave identification command (4/4)
Master
Slave 0x10 identification
Slave 0x10
Slave 0x10
Slave 0x10 returns unique ID
Invalid CRC. Probable cause is multiple slaves with ID = 0x10
Reset Slave ID 0x10
Mask is 0b00000000000000001000000000000000
Slave 0x04
Slave 0x0A
Note that slaves should take a random ID between 1 and 33

## Slide 14: Get the description of an option
Broadcast not supported
Retrieve the description of an option in encrypted JSON format
Index of the option address space starts at 0x20. Return an error if option index is out of bounds.
If option is successfully retrieved, option information will be stored in address space 0x200-0x2fe.
Return the memory size of the option information in the storage.
Modbus QUERY | Value | Description
Slave address | 0x01 | Target slave with this ID
Function | 0x04 | Read Input Registers
Starting Address Hi | 0x00 | Get option1 info. cmd.
Starting Address Lo | 0x21 | Get option1 info. cmd.
No. of Points Hi | 0x00 | 
No. of Points Lo | 0x01 | 
Error Check | CRC | 
Ask slave 0x01 to retrieve description of Option[1]

## Slide 15: Error messages
Error message will occur when:
  Accessing an invalid memory space in R/W
  Providing an invalid argument to the command
  When reading at an invalid space, specify the “Byte Count” field at zero.
  When writing at an invalid space, specify the “No. of Registers” field at zero.
Error will typically indicate that no data have been read or written
Modbus ANSWER | Value | Description
Slave address | 0x01 | Target slave with this ID
Function | 0x04 | Read Input Registers
Byte Count | 0x00 | *** ERROR ***
Error Check | CRC | 
Typical Read error packet

## Slide 16: Options
Options | Unit | Range | Dimension | Function | Write for all slaves | Example
Position_b1 | mm/10 | [0,6000] | 2 | Read/Write | No | [105,1001]
Position_b2 | mm/10 | [0,6000] | 2 | Read/Write | No | [105,1001]
Speed Levels_b1 | mm/s/10 | [0,990] | 4 | Read/Write | Yes | [20,105,55,10]
Speed Levels_b2 | mm/s/10 | [0,990] | 4 | Read/Write | Yes | [20,105,55,10]
Vthresh_b1 | v/10 | [-250,250] | 4 | Read/Write | Yes | [-50,50,-10,40]
Vthresh_b2 | v/10 | [-250,250] | 4 | Read/Write | Yes | [-50,50,-10,40]
Rescale_b1 | 1/100 | [0,1000] | 2 | Read/Write | Yes | [50,170]
Rescale_b2 | 1/100 | [0,1000] | 2 | Read/Write | Yes | [50,170]

## Slide 17: Option Description
{
"name": "Position_b1",
"type": "uint16",
"min": 0,
"max": 6000,
"scale": 10,
"access": "RW",
"dim": 2,
"unit": "mm",
"address": 768,
"broadcase": "false"
}
Example of JSON generated for option “Position_b1”
Note that scale is used by the GUI

## Slide 18: Encryption of configuration section
Configuration section is encrypted using the RC4 algorithm (https://en.wikipedia.org/wiki/RC4)*
  The Key is the 64 bits unique ID
Master can decrypt configuration section as unique ID can be retrieve with Slave Identification command
* Example of C implementation: https://gist.github.com/rverton/a44fc8ca67ab9ec32089

## Slide 19: Firmware update (2/4)
Broadcast not supported
Prior to firmware update, binary data should be uploaded in memory range 0x106-0xFFFF
Hash code is using HAVAL algorithm (128 bits / 3 passes) https://en.wikipedia.org/wiki/HAVAL
If hash code is correct, device return a valid answer and perform the update
Otherwise, it sends an error answer
Slave 10 returns its 64 bits unique ID
Modbus QUERY | Value | Description
Slave address | 0x10 | Target slave(s) with this ID
Function | 0x10 | Preset Multiple Registers
Starting Address Hi | 0x00 | 
Starting Address Lo | 0x10 | Firmware update command
No. of Registers Hi | 0x00 | 
No. of Registers Lo | 0x02 | Two 16 bits registers are required to store the mask
Byte count | 0x14 | 20 bytes
Address (2 bytes) | 0x0160 | Starting address of firmware binary location
Length (2 bytes) | 0xXXXX | Length of firmware binary
Hash (16 bytes) | … | Slave ID 1 and 2 are already attributed.
Error Check | CRC |